## Slide 1
Smart Chicken Coop
An Automated Monitoring & Control System
Raspberry Pi 5 · Python · PCA9685 Servo Driver · 7 Automated Systems

## Slide 2
The Story
Why We Built This
We have a chicken coop at home with six hens. Every single day, someone had to walk out and physically check on them.
Was the water topped up? Had the door closed at dusk? Was it getting too hot inside? Had they run out of food?
If we forgot — the chickens could overheat in summer, run out of water, or be left exposed to predators overnight.
We decided to build a system that manages the coop automatically, so we can check on it from our phones instead of going outside every day.
Daily Tasks — Before Automation
Check & refill water drinker
Every morning
Open coop door at sunrise
Every morning
Close coop door at sunset
Every evening
Check temperature in summer
Hot days
Check food hopper level
Every few days
Turn run lights on/off
Daily

## Slide 3
7 Automated Systems
Temperature
Monitor
DHT22 sensor
Vent Sliders
2× MG996R servo
Circulation
Fan
12V PC fan
Water Level
Monitor
Float switches
Automatic
Door
Linear actuator
Automatic
Lights
LED strips
Food Level
Indicator
Lever + pot

## Slide 4
The Hardware
Raspberry Pi 5
Brain of the system
Runs all the Python automation code
64-bit quad-core CPU
Fast enough to handle all sensors at once
WiFi built in
Serves the debug web panel on your network
40-pin GPIO header
Connects to sensors, relays, and motor drivers
I2C + SPI buses
Talks to the PCA9685 and MCP3008 chips
Pi 5 note
Uses the new RP1 GPIO chip — needs lgpio library, not RPi.GPIO
PCA9685 — Servo Driver
Same board used in the workshop dust collection system.
Connects to Pi via I2C (just 4 wires). Controls up to 16 servos from a single board. We use channels 0 and 1 for the two vent sliders.
MCP3008 — Analog Input Chip
The Pi 5 has no analog input pins, so it can't directly read sensors that output a voltage (like the LDR or potentiometer).
The MCP3008 converts analog voltages to digital values over SPI. 8 channels — we use 2: one for the light sensor, one for the food lever.

## Slide 5
Temperature & Ventilation
How It Works
1
DHT22 reads every 10 sec
Measures temperature and humidity inside the coop
2
Above 27°C — vents open
Two MG996R servos (via PCA9685) push the vent sliders open
3
Below 25°C — vents close
2°C gap prevents the servos from constantly toggling
4
Above 30°C — fan on
12V PC fan switches on via relay to push fresh air through
5
Below 28°C — fan off
Fan stays off below this to avoid overcooling
Hardware
DHT22 sensor
GPIO4 — single-wire protocol
2× MG996R servo
PCA9685 CH0 + CH1
120mm 12V PC fan
12V rail via relay on GPIO17
if not vents_open and temp >= 27:
set_servo(CH0, SERVOMAX)
set_servo(CH1, SERVOMAX)
vents_open = True
if not fan_on and temp >= 30:
fan.on()
fan_on = True

## Slide 6
Automatic Chicken Door
How It Works
1
LDR reads light level
Photoresistor + 10kΩ divider feeds voltage to MCP3008 channel 0
2
Dawn detection
When light reads above 0.60 (bright) the door should open
3
Dusk detection
When light reads below 0.30 (dark) AND it's after 8pm
4
Clock backup
On overcast days the LDR may not trigger — door forces open by 9am
5
Linear actuator
L298N H-bridge drives actuator forward (open) or backward (close)
6
Limit switches
Two micro switches stop the motor when the door reaches each end
Hardware
LDR + 10kΩ resistor
Voltage divider → MCP3008 CH0
12V linear actuator
4-6" stroke, 50-100N, self-locking
L298N H-bridge driver
GPIO5 IN1, GPIO6 IN2
2× micro limit switch
GPIO16 (open end), GPIO20 (closed end)
light = ldr.value # 0.0-1.0
is_dawn = (light >= 0.60 or
hour >= 9)
is_dusk = (light <= 0.30 and
hour >= 20)
if is_dawn: open_door()
if is_dusk: close_door()

## Slide 7
Water Level Monitor
How It Works
1
3 float switches mounted vertically
One at Low, one at Mid, one at Full height inside the water container
2
Float rises with water level
When water reaches a switch, the float lifts and closes the circuit
3
Pi reads each switch
The highest active switch determines which LED lights up
4
Green = Full
All three switches active
5
Yellow = Mid
Only low and mid switches active
6
Red = Low / Empty
Only the lowest switch, or none — time to refill
Hardware
3× vertical float switch (NO)
GPIO22 low / GPIO23 mid / GPIO24 high
Red LED
GPIO25 — low/empty
Yellow LED
GPIO27 — mid level
Green LED
GPIO18 — full
if water_high.is_active:
led_green.on() # Full
elif water_mid.is_active:
led_yellow.on() # Mid
elif water_low.is_active:
led_red.on() # Low
else:
led_red.on() # Empty

## Slide 8
Food Level Indicator
How It Works
1
Lever arm sits in the food hopper
One end of the arm rests on top of the food. As food is eaten, the arm drops
2
Potentiometer at the pivot point
As the lever rotates, the pot wiper moves — outputting a different voltage
3
MCP3008 reads the voltage
Converts the analog voltage (0–3.3V) to a digital value (0.0–1.0)
4
1.0 = full, 0.0 = empty
After fitting the lever, FOOD_LOW_THRESHOLD in config.py is calibrated
5
Below 25% — red LED on
Exterior panel light turns red, visible from outside the coop
6
Above 25% — green LED on
Green means the hopper has enough food
Hardware
10kΩ rotary potentiometer
Mounted at lever pivot → MCP3008 CH1
Lever arm
Custom-built, sits in the feeder hopper
Red LED + 220Ω
GPIO21 — needs food
Green LED + 220Ω
GPIO14 — food OK
# MCP3008 reads 0.0 (empty)
# to 1.0 (full)
food_level = food_pot.value
if food_level < 0.25:
food_led_red.on()
food_led_green.off()
else:
food_led_green.on()

## Slide 9
Automatic Lights
How It Works
1
Two separate light circuits
One for the interior of the coop, one for the outdoor run area
2
Schedule set in config.py
Default: on at 6:00am, off at 10:00pm. Change the hours without touching the code
3
Pi checks time every 10 seconds
Uses Python datetime — no external RTC needed because Pi 5 syncs via WiFi NTP
4
Relay switches the 12V circuit
Pi GPIO drives a 5V relay that controls the 12V LED strip — safe separation of voltages
5
State tracking prevents flicker
The code only switches when the state actually needs to change
Hardware
12V warm white LED strip
Coop interior — 2-3m
12V warm white LED strip
Run / outdoor — 3-5m
2× 5V relay module
GPIO19 coop / GPIO26 run
mins = now.hour * 60 + now.minute
on_min = 6 * 60 # 6:00am
off_min = 22 * 60 # 10:00pm
should_be_on = on_min <= mins < off_min
if should_be_on and not lights_on:
coop_light.on()
run_light.on()

## Slide 10
The Code
config.py
All the settings in one place — temperature thresholds, GPIO pin numbers, servo pulse values, light schedule times. Nothing is hardcoded in the main file. To change when the lights come on, you just edit one number here.
coop_controller.py
The main automation loop. Runs forever, waking up every 10 seconds to read sensors, check time, and update outputs. Each system is its own small function. The Pi 5 runs this as a system service that starts on boot.
debug_panel.py
A Flask web server that serves a control panel on your home network. Open it on any phone or laptop to manually trigger any system, see live sensor readings, and read the log — without touching the Pi.

## Slide 11
Debug Panel — Manual Control
During build and testing, we needed a way to trigger any part of the system manually without writing temporary code. We built a web-based control panel that runs on the Pi.
Live sensor readings
Temperature, humidity, light level, food %, water level, and both door limit switch states — all auto-refreshing every 5 seconds.
One-click manual control
Buttons for every system: open/close vents, fan on/off, door open/close/stop, coop lights and run lights.
Emergency door stop
A dedicated STOP button that immediately cuts the door motor — useful when testing the actuator travel before the limit switches are fitted.
Live log viewer
The last 50 lines of coop.log shown on the page, with a Refresh button. No need to SSH into the Pi to see what the controller is doing.

## Slide 12
What We Learned
Real hardware is harder than code
Getting sensors to read reliably outdoors — temperature, humidity, light — took more calibration than the software logic.
The Pi 5 is different
The new RP1 GPIO chip broke the old RPi.GPIO library. Switching to lgpio and understanding why took real debugging.
Hysteresis matters
Without a gap between on/off thresholds, the vents and fan would toggle constantly. Small design choices have big real-world effects.
Separation of concerns
Putting all configuration in config.py and keeping the logic in coop_controller.py made the code much easier to change and test.